## Slide 1
QVoice feasibility evaluate
Reported by Arthur ,Allen, BJ
Report Date:2017 / 12 / 20

## Slide 2: SHS0017W Features

## Slide 3: SHS0017W Block Diagram

## Slide 4
No |  | Yes/No
1 | User Experience Design | Y
2 | Hardware | Y
2.1 | Hardware Development | Y
2.2 | ID Design | Y
3 | Software | Y
3.1 | Core Software Development | Y
3.2 | WEB UI | N
3.3 | Mobile App | Y
3.4 | Cloud | Y
3.5 | Tools | Y
4 | Accessories | Y
4.1 | Cables | Y
4.2 | Quick Start Guide | Y
4.3 | Manuals | Y
4.4 | Regulation Papers | Y
5 | Support | Y
5.1 | Support Process | Y
5.2 | Self Care + FAQ | Y
6 | Marketing | Y
6.1 | Packaging | Y
6.2 | Datasheet | Y
6.3 | WEB + PR | Y
7 | Product Management | Y
7.1 | Product Presentation | Y
7.2 | Roadmap | Y
7.3 | Business Plan | Y
8 | Integration Testing | Y
9 | User Experience Testing | Y
Fill this Out!
1. Project/Product Components
User Experience Design
Software
Marketing
Accessories
PM
Support
User Experience Testing (Friendly User Test with Samples)
Integration Testing
1
2
3
4
5
6
7
Hardware
8
9
Initial Task for Project Manager + Sponsor:
Decide if needed or not needed in your project
Plan accordingly
Hardware Dev.
ID Design
Core Software
WEB UI
Mobile App
Cloud
Cables
Manuals
Regulation Papers
Quick Start Guide
Packaging Design
Datasheet/Flyer
WEB + PR
Product Presentation
Roadmap
Support Process
Self Care + FAQ
Business Plan
Tools
7.2
7.1
6.3
6.2
6.1
5.2
5.1
4.4
4.3
4.2
4.1
3.5
3.4
3.3
3.2
3.1
2.2
2.1
7.3
What is the end-users Total Experience for every step of the Journey?
User Research (Who are the Users and how do they use it?)
Usabilty (can you achieve the product goal in a simple way?)
Interaction (how pleasant is it to interact with the device?)
Visual Design (The well-considered look and feel of everything)

## Slide 5: 2. Project Charter
Project ID / Name | SHS0017W-D249(RoHS)/ QBee voice | 
Project Goal | Develop Askey standard Voice Personal Assistant for promoting to our customer.(NOS, SingTel) | 
High Level Scope | 1. Qvoice can use IoT device(Amazon qualification) skill directly. 2. Q&A | 
Deliverables | Demo Concept: QBee voice(SHS0017W) connect to QBee box to control IoT device. IoT Device list: Z-wave devices. (Bulb, Plug, Switch); Control way : a. Voice b. App | 
Milestones | HW:ES build 2nd SMT: 2017/12/09 (50pcs) 10 pcs send to TPE: 2017/12/28 SW: Use Qvoice through the cloud and Qbeehome to control IOT devices, including Z-wave and Bluetooth mesh devices. | 
Estimated Costs | Safety test(LVD):RMB 6,000 EMC(CE): RMB 112,000 Environmental Impact Assessment: USD 1,900 Tooling fee: USD$55,000 Mock up fee: NTD $88,200 Human resource: NTD$ 25,004,000 Production factory line: NTD 196,300 Sample cost: USD$24.42 * 220 = USD$ 5372.4 Total:NTD $27,759,049 | 
(Potential) Customer(s) | NOS, SingTel | 
Vendors / Partners | HW: Realtek: RTL8197, RTL8822, ALC5680 | SW: SW team: Arichi team. Cloud: Cloud (Archer) APP team (Kings)
Review and Approval (Key Stakeholders) | Project Manager: B.J. Lee Product Manager: _Allen Chung_________ Project Sponsors: ___Robert Lin______________________ | 

## Slide 6: 3. Project Organization
Sponsor+
Steering Committee
Robert,Eric,Alan,Auger,Arthur,Frank
Project Manage
PJM/B.J. Lee
Software Manager
SWPM/Taimin
MERD Daniel
HWRD Yuzhao
UX/UI
Amiga
Product Manger
PLM/Arthur
PLM
Allen Chung
HWRD Wei
cheng
PCB Layout Abel Zou
ID
Adam Lin
Thermal
Kevin Huang
PKG
Design Erin Yang
Label
Design Wei Hou
SW APP
Jason1 Su
SW Driver
Ryan Hsu
SW Driver
Wilson Hung
SW APP
Leo2 Cheng
SW APP
Cooper1 Chen
SW APP
Indy Hsiao
SW Cloud
David5 Huang
SW Cloud
Thomas Wong
Product line Control
Jian Xu
Material
Control
Davy Lee
IE
Ming Liu
Produc TE
Boyce Dong
SQC
Amy Xu
PQC
Weiping Yu
OQC
Ameer Zuo
CQC
Yee Yi
RDTE
Lester Lin
HW SIT
Juan Chu
SW SIT
Peichun Wu
SW SIT
Randy Hsu
DQA
Quanhua
QTR
Vickiya shen
MPM
Sheila Wu
EMC
Lino Zhu
Safety
Chen Lin
Marketing
Cecile Hanel
Support
Operation
FPM/Andre
SW SIT
Peter2 Chang
SW Driver
Jada Lin

## Slide 7
Mobile App
MQTT Mobile APP
Message handler
UI handler
Hardware
Software
Message contents in MQTT packets are Askey proprietaries.
MQTT message flow
AWS IoT
Home gateway
QVoice
Linux kernel
Hardware
Software
Alexa client
AVS
AVS message flow
MIC, SPK and codec
QBee Home
Applications
Z-wave control APP
(Askey)
MQTT Agent APP
MQTT
Local server
Zwave module
Framework, Library, and Kernel
Bluetooth module
Zwave handler
Message handler
BT Mesh handler
BT MESH control APP
(Askey)
CES Show:
QBee Home + Qvoice

## Slide 8: 4. Project Milestones Overview
Project ID/Name | SHS0017W-D249 / QVoice | Date: | 20 Dec. 2017 | Overall Status | 
Components |  | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun |  | Jul
1. UX Design |  |  |  |  |  |  |  |  |  |  |  |  | 
2. H/W | 2.1 Hardware dev. |  |  |  |  |  |  |  |  |  |  |  | 
 | 2.2 ID Design |  |  |  |  |  |  |  |  |  |  |  | 
3. S/W (before CES) | 3.1 Device SW |  |  |  |  |  |  |  |  |  |  |  | 
 | 3.2 Cloud 3.3 SW SIT |  |  |  |  |  |  |  |  |  |  |  | 
S/W (Standalone) | 3.4 Device SW |  |  |  |  |  |  |  |  |  |  |  | 
ES
Mock up x14pcs
1. bring up 8197+5680 EV 2. ALC5680可收wake word
LWA & AVS Skill modification
User Experience Design
Hard tooling start TBD
Milestone 1
15th Dec. 2017
Milestone 2
26th Jan. 2017
QA
EV
QA
DV
QA
PV
QA
Mock up-16pcs
1. AVS control 2. fix WPS and Reset 3. incl. bootcode & root file system
Integrate with Z-wave & BT
Auto Refresh token, WPS, Telnet
Milestone 3: Launch
2nd May 2018
12/26
5/2
RD SIT for Qvoice only
Dual image, IPV6
RD function test and formal release test
Support production line and test FW
RD function test and formal release test

## Slide 9: 4. Project Milestones Overview
Project ID/Name | SHS0017W-D249 / QVoice | Date: | 04 Dec. 2017 | Overall Status | 
Components |  | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun |  | Jul
4. Accessories | 4.1 Cables/adaptor |  |  |  |  |  |  |  |  |  |  |  | 
 | 4.2 Quick Start Guide |  |  |  |  |  |  |  |  |  |  |  | 
 | 4.3 Manuals |  |  |  |  |  |  |  |  |  |  |  | 
 | 4.4 Regulation Papers |  |  |  |  |  |  |  |  |  |  |  | 
5. Support | 5.1 Support Process |  |  |  |  |  |  |  |  |  |  |  | 
 | 5.2 Self Care + FAQ |  |  |  |  |  |  |  |  |  |  |  | 
6. Marketing | 6.1 Packing Design |  |  |  |  |  |  |  |  |  |  |  | 
 | 6.2 Data Sheet |  |  |  |  |  |  |  |  |  |  |  | 
 | 6.3 WEB + PR |  |  |  |  |  |  |  |  |  |  |  | 
7. PM | 7.1 Product Presentation |  |  |  |  |  |  |  |  |  |  |  | 
 | 7.2 Roadmap |  |  |  |  |  |  |  |  |  |  |  | 
8. Integration Test |  |  |  |  |  |  |  |  |  |  |  |  | 
9. UX Testing |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop
TBD
QA
TBD
TBD
Infrastructure
TBD
Proposal
Infrastructure
Testing Script
Unit Test
Integration Test
Friendly User Test (6 samples ready for Qbee box integration testing)- pending
TBD
TBD
QA
QA
QA
Launch
Milestone 2
26th Jan. 2017
Milestone 3: Launch
2nd May. 2018
CES
QA
Procurement
QA
QA
QA
Milestone 1
15th Dec. 2017

## Slide 10: SHS0017W Software Features
Voice assistance
  Basic AVS Q&A
  Sing a song
  Alarm/Timer
  Streaming (play ICRT, podcast, news….)
  Volume up / Volume down / mute / un-mute
  Support Amazon skills (translation, …….)
  Support IoT devices control (e.g. Lutron turn on/off light, TV controller on/off…..)
Network
  Ethernet 10/100/1000M bps
  Web download
  Telnet function
WIFI
  WI-FI 2.4g/5g AP/station mode (802.11b/g/n)
  WPS server/client mode function
  IPv4, IPv6
Dual image
In the future:
Network security/firewall (防火牆預防網路攻擊)
Support UPnP
Bluetooth functions
  Connect to speaker / home sound system

## Slide 11: QVoice SW Check Points For CES Show
CES show (2018/1/9~12)
SIT integration test stage
RD development stage
2017
October
November
December
January
2018
10/24 release test image
1. 5680可收wake word
2. 8197 Alexa client can control device and general reactions
10/23 ~11/3 AVS Status control
(Led shine: connecting to AVS,
Led off: connected to AVS success )
11/6~11/10
* Login with amazon and mapping to Askey User Account (Cloud Team Only)
* AVS Skill for CES scenarios (I) single device
11/10 ES sample (16 pcs for SW)
11/3 ~11/17
check and fix WPS & reset to default button .
11/20 ~ 11/30
include bootcode and root file system in a burn file (only include bootcode currently).
11/20~11/30
Integration test with z-wave devices and BT devices.
11/13~11/17
* AVS Skill for CES scenarios (II) multiple devices ( living room light + kitchen light )
* AVS Skill for CES scenarios (III) all devices (leave or back)
10/23:
RD SIT test V335 (1023v)
11/25~12/15
RD debug for Integration test
11/1~11/3:
RD SIT test V335 (1101v)
11/22 RD test 1122v @ Askey PCBA
12/04~12/08
integration test
12/01~12/15
RD debug for integration test
12/15
Qvoice device sw fixed version
12/15
Cloud sw fixed version
11/16
RD SIT test V335 (1115v)
11/27 RD test 1127v @ Askey PCBA
12/11~12/15
integration test

## Slide 12: Standalone Functions Development
11/24
Archi team
Cloud team
Mobile app
Jada team
11/30
11/20~11/30:
Auto refresh token
11/22~11/24:
Telnet function
11/13~11/24:
WPS function
12/01~12/15: dual image:
1. Partition
2. Generate firmware image for burning
3. Firmware upgrade
12/04~12/13
IPv6 module in Kernel
12/15
11/26~11/27:
Web download for single
12/13
11/27
12/18~12/31:
Support production line and test software development
Fix bug and fine tune firmware.
12/18~12/31
Support production line and test software development
Fix bug and fine tune firmware.
12/31

## Slide 13: 5. Project Risks
Project ID/Name |  | QVoice |  |  |  |  |  | Reporting Week | CWNN | 
Risk Nr. | Date Identified | Category | Description | Probability Level | Impact Level | P*I | Response | Contingency Plan | Risk Owner | Status
001 | 2017/11/28 | HW | WiFi will be drop line after write RF calibrated data into Qvoice | 3 | 4 | 12 | PJM/BJ | HW tried to tune RF matching as FAE suggestion. Realtek agree us deliver one board to debug in Realtek’s RD. | Yuzhao | ES
002 | 2017/12/04 | HW | Observe No3 sample poor voice recognize with Flypower’s PSU. | 3 | 4 | 12 | PJM/BJ | 1. First step validated Flypower PSU (it will drop to 4.45V). 2. Phihong PSU will deliver to WJ HWRD on Dec.25 | Yuzhao | ES
003 | 2017/12/20 | FW | Build code version control | 4 | 3 | 12 | PJM/BJ | 1. It needs to align with different SW team. 2. Use bitbucket to sync and control software. | SWPM / Taimin | ES

## Slide 14: 5.1 Solved Important Issues
Project ID/Name |  | QVoice |  |  | 
Issues Nr. | Date Identified | Category | Title | Status | Description
001 | 2017/12/01 | FW | Cannot sign a song | Solved | The function support in current firmware (1215 toggle)
002 | 2017/12/01 | FW | Timer/Alarm cannot give an indication | Solved | The function support in current firmware (1215 toggle)
003 | 2017/12/01 | FW | 連續做2次串流播放, 第2次的串流無法播放. | Solved | The function support in current firmware (1215 toggle)
005 | 2017/11/30 | FW | Include bootcode and root file system in a burn file | Solved | Realtek release patch, askey RD test OK.
006 | 2017/12/04 | FW | AVS always wait (LED 恆亮問題) | Verifying | 之前網路狀況不好，此問題時常存在 經過AVS client優化，此機率已降為 6/800 = 0.75%
007 | 2017/11/22 | FW | 語音指令Volume UP / Volume Down / Mute / Unmute 有機會失敗 | Verifying | 經過AVS client優化，成功機率： Alexa, Volume Up: 90% (9/10)  100 % (100/100) Alexa, Volume Down: 90% (9/10)  100 % (100/100) Alexa, Mute: 100% (10/10)  99 % (99/100) Alexa, Un-mute: 80% (8/10)  100 % (100/100) 總失敗機率從10%降為 1/400= 0.25%

## Slide 15: 5.2 HW test plan
12/21: FW release – fix 2.4GHz EVM issue
12/22: HW pretest
12/26: HW/SW freeze version for ES HW testing.
1/28: First round HW items test in ES phase.

## Slide 16: 距離辨識效能測試
[Askey QVoice(7號)距離辨識效能測試]
測試機台 ：QVoice Askey標準品(7號) v.s. Amazon Echo Dot (測試對照組)
FW version：bootloader：shs0017w_boot_dual_static_20171201.bin
kernel：shs0017w_fw_dual_RTK_patch_20171204.bin
HW version：Askey QVoice 標準品(編號7)
量測方式 1(Quiet)：以平板電腦發出固定的Wake Word指令：Alexa, 在直線1公尺、3公尺、5公尺等距離,做測試機台辨識成功率統計
量測方式 2(Noise)：以平板電腦發出固定的Wake Word指令：Alexa, 並且在斜角45度 2公尺處放置Noise Speaker(電腦以固定音量播放音樂),
在直線1公尺、3公尺、5公尺等距離,做測試機台辨識成功率統計.
(環境音量約40分貝、平板電腦發出Wake Word音量約60分貝、Noise Speaker發出的音樂音量約50~70分貝)
[測試結果]:
由下表測試結果, Askey QVoice(編號7)在有噪音下的”Alexa Wake Word喚醒”測試結果, 略優於 Amazon Echo Dot.
[驗證結果如下]:

## Slide 17: QVoice 應用場景 – IP分享器 + 語音助理
Pocket size (家用旅行都方便)
支援路由器, 基地台(AP), 中繼器 (repeater)
最新 802.11ac 無線技術 (相容於 802.11 a/b/g/n), 2.4G/5G 雙頻同步
支援雲端服務可遠端管理
智慧防盜 (出門在外時可遠端遙控開關燈、放音樂, 營造有人在家的氛圍)
智慧教育 (即時英語對話, 訓練聽說能力)

## Slide 18: Qvoice Control Lutron IoT Device Demo
Scenario:
  Basic Q & A
  IoT control
      Alexa, turn on the (office) light.
      Alexa, dim the office light.
      Alexa, set the office light to 20 percent.
      Alexa, turn off the (office) light.
LTE router
QVoice
Lutron IoT GW
Lamb
Lutron IoT

## Slide 19: QVoice軟體人力規劃
QVoice SW
SW SIT
Cloud
QVoice
Device SW
于岱民
蕭有廷
鄭協龍
陳楷富
吳家豪
紀彥丞
姜依帆
黃郁茹
林毓達
洪俊原
許裕昇
張堯翔
吳佩君
許哲維
黃智敏
黃士帆
陳品宏
11
3
3
17

## Slide 20: System Architecture (Voice Assistant)
RTL 8197 + RTL 8822 + ALC5680
Linux Distribution
OpenSSL
ALSA Library
Askey library
HTTP Client Library
libcurl
Authentication
Device Config.
HTTP/2
Wake Word Handle
Request Message
Response Message
Alerts processing
Audio player processing
Context processing
Alexa Settings
Speechrecognizer Processing
Speechsynthesisizer processing
Alexa C Client
Get refreshtoken
(registration)
Web server for setup
ALSA config for microphone & speaker
Wake word engine
Sensory lib
WakeWordDetected()
Askey Customized
RealTek alexa client
Open source library
Linux
Hardware
Askey porting
Wake word engine
MQTT Client/Server

## Slide 21: Cloud Architecture for Alexa
Project Customized
service
Askey Cloud Component Service
AWS Service
OAuth Aggregate
Identity Service Connect (LWA)
Device Registry
IoT Rule Engine
Columnar Storage
IoT Rule
NO SQL
MQTT Server
Web Server
CDN Service
DNS Service
Cross AZ backup
FOTA Service
Object Storage
System Auditing
Smart Things Service
Data Pipeline
Data ETL
Skill Lambada/
CES excel
HAP Biz Console
Version Update Service
Biz Console API
Device Enrollment